## Slide 1
PROJECT REVIEW, PHASE 1 · 9 OCTOBER 2026
ecu_soc
A RISC-V HARDWARE ECU (SOC) FOR A SELF-BALANCING ROBOT
From RTL to FPGA validation to layout (RTL-to-GDSII)
Dept. of VLSI Design & Technology,
Goa College of Engineering
Team: Jatin, Kaushal, Dipiksha, Vedam, Jaydev
Guide: Dr. Sonia Kurade

## Slide 2
PART A
PROJECT CONTEXT
& DESIGN
OBJECTIVES

## Slide 3
WHAT IS AN ECU?
Electronic Control Unit: a small embedded system that senses, decides and acts within fixed time limits.
Sensors
Sense →
ECU
I2C · Filter · PID · PWM · safety · CPU
Core · memory · sensor interfaces · actuator drivers · timers · safety logic
Actuators
→ Act
Vehicles carry many: powertrain, safety, body control, HVAC, lighting, keyless entry.
Ours: a compact ECU designed as an SoC, controlling a self-balancing robot.

## Slide 4
PROBLEM STATEMENT
A two-wheeled balancing robot is unstable: measure tilt and correct within milliseconds.
TYPICAL
Single MCU
Software loop on a general-purpose MCU
Timing jitters with firmware
Safety shares the processor
Commercial ECUs are closed
OUR APPROACH
Hardware loop
Compact, transparent ECU SoC
Dedicated hardware, fixed latency
Small RISC-V CPU configures and supervises
Independent hardware safety cuts motors
Fixed-latency sensing to PWM · CPU out of the real-time loop · Verified in simulation, validated on FPGA, carried through layout

## Slide 5
OBJECTIVES AND SCOPE
01
Synthesizable RTL
Verilog for every ECU block; verified against a reference model.
02
Real-time datapath
I²C IMU, calibration, filtering, fixed-point PID, PWM.
03
Hardware safety
Tilt, sensor loss, watchdog, E-stop.
04
Ibex RISC-V
Core, memory and memory-mapped bus.
05
FPGA validation
Block-by-block, then full ECU on a balancing robot.
06
Physical design
Cadence RTL-to-GDSII flow.
In scope: single-axis PID balancing, one IMU, two DC motors.
Future: LQR/MPC, outer loops, wireless, multi-axis.
Objectives are targets; outcomes reported with measured numbers.

## Slide 6
PART B
CONCEPT,
METHODOLOGY
AND POSITIONING

## Slide 7
THE INVERTED PENDULUM
A rod balanced upright is an unstable equilibrium: any small tilt grows.
Small-angle model: θ̈ ≈ (g/l)·θ − (1/l)·a
Error grows about 2.7× every √(l/g); for l = 15 cm, that is about 0.12 s.
Controller reacts in tens of milliseconds.
Body = pendulum · wheels = movable pivot
Motors = acceleration · IMU = tilt sensor

## Slide 8
THE BALANCING LOOP: SENSE, COMPUTE, ACT
Lean forward, drive forward; lean back, drive back.
512 Hz
One pass every about 1.95 ms
Under 5 µs
Hardware; sensor read about 0.4 ms
About 3 ms
Sensor low-pass dominates delay
Handles pushes, uneven floor, battery changes, sensor noise.

## Slide 9
WHY PID: CONTROL STRATEGY
Small deterministic hardware block; needs only the IMU. Gains live in registers, so tuning needs no re-synthesis.
OPTION | NEEDS | COMPLEXITY | COMMENT
PID (chosen) | angle + rate | low | simple, fixed-point friendly
Fuzzy-tuned PID | angle + rule base | medium | extra logic
LQR / state feedback | model + encoders | medium-high | more sensors, matrix maths
MPC / adaptive | model + optimiser | high | overkill here

## Slide 10
SENSING AND ANGLE ESTIMATION
Baseline: accel tilt, gyro rate for the derivative term, short moving average.
Option: shift-only complementary filter.
Sensor: MPU-6050 over I²C.
APPROACH | STRENGTH | WEAKNESS
Accelerometer only | no drift | noisy under acceleration
Gyroscope only | smooth, fast | drifts
Complementary filter | cheap, combines both | one tuning constant
Kalman filter | optimal | heavy compute

## Slide 11
WHY A HYBRID IMPLEMENTATION PLATFORM
Latency is fixed by structure; the CPU configures but cannot disturb timing.
PLATFORM | TIMING DETERMINISM | SOFTWARE-INDEPENDENT SAFETY | CONFIGURABLE | EFFORT
A. Software PID on MCU | firmware-dependent | no | high | low
B. Fixed-function FPGA only | high | possible | low | medium
C. Soft-core CPU does all | software-dependent | no | high | medium
D. Hardware datapath + RISC-V supervisor (ours) | high, fixed in clock cycles | yes | high (registers) | higher
The cost: more design and verification work.

## Slide 12
LITERATURE SURVEY
Prior work shows how PID works, FPGAs help, and RISC-V is entering ECUs. We combine these in a small, open platform.
REF | WHAT WAS DONE | GAP VS OUR GOAL |  | 
R1 Ordóñez Cerezo 2019 | PD in open-source FPGA; IMU read via Arduino Nano | external MCU, no integrated CPU |  | 
R2 ICM³ 2026 | ESP32 + MPU-6050 + complementary filter + PID (Kp 25, Ki 0.8, Kd 10); settles in 1.5 to 2 s | software loop, no hardware determinism |  | 
R3 Langley 2016 | myRIO FPGA with PID loops | commercial platform |  | 
R4 Abdel-Hady 2025 | multibody model + PID, LabVIEW FPGA | vendor tool flow |  | 
R5 Undip | ATMega16 + MPU-6050, fuzzy-tuned PID | MCU software only |  | 
R6 IEEE survey | FPGA accelerators suit latency-critical robotics | survey, not a full SoC |  | 
R7 arXiv 2023 | RISC-V automotive ECU; interrupt-latency gap | high-end automotive focus |  | 
R8 Ibex (lowRISC) | small 32-bit RV32IMC core | a core, not a system |  | 

## Slide 13
IS ANYONE ELSE DOING SOMETHING SIMILAR?
Dedicated hardware for the time-critical loop. A CPU for management.
TI C2000 control-law accelerator runs independent of the main CPU [R10]
RISC-V motor drives with hardware FOC [R11]; Codasip RISC-V with CORDIC accelerators [R12]
SignOff REV-E dual-core RISC-V controller [R13]; Infineon RISC-V automotive MCU [R14]
The architectural idea is established in industry.
Not found in a limited search: an open, small-scale reference combining RISC-V supervisor, hardware PID, CPU-independent safety and a documented flow to layout.
We are not competing with these products. We build a transparent, student-scale reference of the same proven pattern.

## Slide 14
WHAT IS DIFFERENT IN OUR APPROACH
CPU out of the loop: fixed-latency hardware pipeline, Ibex only supervises
Independent safety monitor: motors off within 2 clock cycles, deliberate re-arm
D term from the gyro rate, with built-in anti-windup
Everything tunable through registers, no re-synthesis
Frozen interface contract: five people build in parallel
End-to-end and documented: simulation, FPGA, layout
The individual ideas are known; what is new is the open, fully documented combination.

## Slide 15
WHY IT FITS, AND THE TRADE-OFFS
ASPECT | SOFTWARE PID ON MCU | OUR HYBRID ECU
Loop timing | varies with firmware | fixed in clock cycles
CPU load | loop uses the CPU | CPU free for supervision
Safety | same CPU as the loop | separate hardware monitor
Tuning | recompile / flash | write registers
Visibility | hidden by libraries | every signal observable
Design effort | low | higher
Changing the algorithm | easy | needs RTL change
Accepted: more up-front effort and a fixed PID structure, for predictability and safety independence. Latency, jitter and fault response will be measured, not assumed.

## Slide 16
PART C
SYSTEM
ARCHITECTURE

## Slide 17
SYSTEM ARCHITECTURE AND BLOCK DIAGRAM

## Slide 18
DATA FLOW, TIMING AND CONVENTIONS
One 50 MHz clock domain, synchronous; each stage passes a 1-cycle valid pulse.
Q16.16 signed fixed-point: ; 0.25 rad = 16384; motor command in [−1, +1].
Every stage finishes within 64 clock cycles; names, widths, formats and addresses frozen team-wide.

## Slide 19
I²C MASTER
MPU-6050 bus master. SCL and SDA are open-drain: pull low or release.
DIV = 31 gives about 390 kHz at 50 MHz.
Bit-level FSM: START, 8 data bits, ACK, repeated START, STOP
Input synchronisers, clock stretching, stuck-bus recovery (9 pulses)
One byte = 9 clocks, about 23 µs; MPU-6050 allows up to 400 kHz
Verified with a behavioural slave model: ACK/NACK, repeated start, stretching. Then ILA.

## Slide 20
I²C MASTER SENSOR SUBSYSTEM

## Slide 21
MPU-6050 CONTROLLER AND REGISTER BANK
START-UP
Wait 50 ms, WHO_AM_I (expect 0x68), wake, set divider, low-pass, gyro ±250 °/s, accel ±2 g.
EACH TICK
One 14-byte burst read from 0x3B: ax, ay, az, temp, gx, gy, gz, high byte first.
SAMPLES
Published together only after STOP.
NACK OR TIMEOUT
Abort, count, skip; 3 in a row: re-initialise.
REGISTER BANK
Enable, clock divider, status, counters, last raw values.
Tick to sample ready: about 0.4 ms.

## Slide 22
TIMER, CLOCK AND RESET
TIMER
About 512 Hz
32-bit counter, programmable period; default 97,656 cycles at 50 MHz.
Outputs: control_tick (1-cycle pulse) and a CPU interrupt every 51 ticks (about 10 Hz).
CLOCK AND RESET
50 MHz
Board oscillator, MMCM.
Reset asserts immediately, releases synchronously, held until the clock locks.
Overrun flag if the sensor is still busy at the next tick.

## Slide 23
MEASUREMENT CAPTURE AND CALIBRATION

## Slide 24
MEASUREMENT CAPTURE AND CALIBRATION
Capture latches all six axes at the same instant; sequence counter for tracking.
Gyro-bias calibration
Robot still: discard 64 samples, average 256 (about 0.6 s), subtract bias from later readings.
A small constant gyro offset integrates into a growing angle error.
FSM: idle, settle, accumulate, done; auto-start in hardware-only test mode.
Safety monitor refuses to arm until calibration is done.

## Slide 25
ANGLE CONVERSION AND ERROR CALCULATION
ACCELEROMETER → TILT
16384 LSB/g converts by ×4 into Q16.16 radians. Small-angle approximation: about 4% off at 0.5 rad, negligible near upright.
GYRO → RATE
131 LSB/(°/s) to rad/s in Q16.16 is about ×8.73. Shift-add ×8.75 gives 0.2% error, with no multiplier.
ERROR CALCULATION
Saturating subtraction; rate passes through to the PID.
MOUNTING AND TRIM
Mounting-dependent axis select and sign-invert bits; balance-point trim register.
WORKED CONVERSIONS
Accel 4096 gives 16384 (0.25 rad); gyro 131 gives 1145.

## Slide 26
DIGITAL FILTER
Moving average of samples, k = 0 to 4; k = 0 is bypass. One instance for angle, one for rate.
Circular buffer + running sum: one add, one subtract, one shift. No multipliers.
More smoothing means more phase lag. Extra delay about samples, about (N-1)ms per step at 512 Hz, on top of the sensor's 3 ms internal filter. N stays small (2 to 8).
OPTIONAL COMPLEMENTARY FILTER
, . Shifts only; selected by a register bit.
STEP RESPONSE · 0 TO 4000
Verification: N = 4 gives 1000, 2000, 3000, 4000

## Slide 27
HARDWARE PID ACCELERATOR: ARCHITECTURE

## Slide 28
HARDWARE PID ACCELERATOR: ARCHITECTURE
INTERFACE
Inputs: error , rate , run-enable from safety. Outputs: motor command in Q16.16, saturation flag.
DATAPATH
P term; I term with clamped accumulator; gyro-rate-based D term; sum and saturate.
SHARED ARITHMETIC
One shared 32×32 multiplier, time-shared by a small state machine, about 8 cycles. Smaller than three multipliers.
REGISTER BANK
Kp, Ki pre-scaled by Ts, Kd, setpoint, integrator limit, output limit, control bits.
Read-only telemetry: P, I, D and output.
LATENCY TARGET
At most 16 cycles
Input pulse to output pulse: about 0.3 µs at 50 MHz.
Gains are registers. The CPU, or a hardware default, can retune live.

## Slide 29
PID ALGORITHM DETAILS
, so (constant setpoint)
ANTI-WINDUP · TWO RULES
Integrator clamped to ±limit.
Integrator frozen while output is saturated in the same direction as the error.
DISABLE
Safety withdraws run-enable: output = 0, integrator cleared, previous error reset. No derivative kick on re-enable.
WORKED CHECKS
Kp = 1.0, e = 0.1 gives u = 0.1.
Kp = 8.0, e = 0.2, limit 0.25 → saturates at 0.25 and raises the flag..
Ki step of 65 counts per sample gives 650 after 10 samples.
FIXED-POINT
Q16.16; 64-bit intermediate product; arithmetic shift (floor); saturating sum.

## Slide 30
PWM GENERATOR

## Slide 31
PWM GENERATOR
20 kHz: period 2500 cycles at 50 MHz, within the BTS7960 limit [R9], above audible range.
Duty: from a small multiplier. Duty and direction update only at the period boundary, with no runt pulses.
Positive to RPWM; negative to LPWM; never both. Dead-time: 250 cycles (5 µs) on every direction change.
Shaping: max-duty clamp, default 0.9 for first tests; optional slew limiter; steering offset; per-motor gain.
Safety gating: enable low gives outputs low within 2 cycles.
WAVEFORM CHECKS
Verification: assert RPWM and LPWM are never high together. Duty checks: command +0.5 gives 1250/2500 counts.

## Slide 32
MOTOR INTERFACE AND BTS7960 DRIVER
FPGA pins
RPWM · LPWM
R_EN · L_EN
BTS7960B module
PWM → driver
Motor
One module per motor
MAPPING AND ENABLE
Motor interface maps PWM channels to driver pins. Per motor: RPWM, LPWM, R_EN, L_EN. Direction-invert bits absorb wiring differences; enable is gated by the safety monitor.
DRIVER [R9]
BTS7960 half-bridge: two modules, one per motor. Integrated driver; PWM up to 25 kHz; typical current limit about 43 A.
Operating supply 5.5 to 27.5 V. P-channel high-side switch, so no charge pump needed.
BUILT-IN PROTECTIONS
Dead-time generation; over-temperature; over/under-voltage; over-current; short circuit.
BRING-UP DISCIPLINE
Logic only first; check waveforms. Motors on a stand, wheels off the ground. Common ground. Verify the module's logic-level compatibility before connecting.

## Slide 33
SAFETY AND FAULT MONITOR: STATE MACHINE

## Slide 34
SAFETY AND FAULT MONITOR: STATE MACHINE
DISARMED
Reset: motors off
→ ARMED: arm request + calibration done; no live or stored faults
ARMED
Motors allowed
→ FAULT: any fault
FAULT
Flag latched
→ ARMED: clear flags, condition gone, arm request toggled low to high
Motors are allowed only in ARMED. Fail-safe default after reset: motors off; turning them off never needs software.
Arming needs arm request, calibration done, no live fault, no stored fault flags.
Any condition drops the motor enable within at most 2 clock cycles (40 ns at 50 MHz); the flag is latched.
Re-arming is deliberate. The robot never restarts by itself.
E-stop is honoured from any state; the optional watchdog detects a stalled CPU.

## Slide 35
SAFETY MONITOR: FAULTS AND RESPONSES
FAULT | CONDITION (DEFAULTS, ALL PROGRAMMABLE) | RESPONSE
Tilt | ¦θ¦ > 0.6 rad (≈ 34°) on 3 consecutive samples | latch, motors off
Sensor timeout | no sample for 8 ticks (about 16 ms) | latch, motors off
I²C error | 3 consecutive failed transactions | latch, motors off
PID saturation | output saturated for 256 samples (about 0.5 s) | latch, motors off
Watchdog | no CPU kick for 100 ticks (about 195 ms), if enabled | latch, motors off
E-stop | external button (active-low) | immediate, motors off
Fault flags readable by firmware; interrupt informs the CPU; thresholds are registers.
Tests: every fault alone, two at a time, glitch rejection (a 2-sample spike must not trip), re-arm sequence.

## Slide 36
MEMORY SUBSYSTEM AND BUS INTERCONNECT

## Slide 37
MEMORY SUBSYSTEM AND BUS INTERCONNECT
INSTRUCTION FETCH
Ibex instruction port → ROM (8 KB)
DATA PORT
Ibex data port → Address decoder → ROM (8 KB), RAM (4 KB) and six register banks
ROM (8 KB): firmware image; two read ports (instruction fetch and constants), loaded from the compiled program.
RAM (4 KB): stack and variables; byte-writable.
Bus: Ibex instruction port to ROM; Ibex data port to address decoder to ROM, RAM and six register banks.
Protocol: request granted in the same cycle; data returns one cycle later (zero wait states); writes are acknowledged too.
Safety net: an unmapped address returns an error response with no side effect, so the CPU never hangs on a bad address.
Sizes are parameters, kept small on purpose (layout-friendly).

## Slide 38
MEMORY MAP, REGISTER BANKS AND TOP LEVEL
REGION | BASE ADDRESS | SIZE
ROM | 0x0000_0000 | 8 KB
Timer | 0x1000_0000 | 4 KB
I²C | 0x1000_1000 | 4 KB
Sensor pipeline | 0x1000_2000 | 4 KB
PID | 0x1000_3000 | 4 KB
PWM | 0x1000_4000 | 4 KB
Safety | 0x1000_5000 | 4 KB
RAM | 0x2000_0000 | 4 KB
REGISTER CONVENTIONS
Every bank starts with a read-only ID word, e.g. "TIM", "I2C", "PID", so firmware can prove the bus works.
Write-1-to-clear status bits; self-clearing command bits; defined reset values.
TOP LEVEL
ecu_soc_top wires all blocks. A HW_ONLY parameter runs the hardware loop without the CPU for early FPGA tests.
FPGA WRAPPER
Clocks, input synchronisers, open-drain I²C buffers, LEDs.

## Slide 39
SOC SYSTEM HIERARCHY

## Slide 40
PART D
THE CPU:
IBEX

## Slide 41
CPU / HARDWARE BOUNDARY
ROLE OF THE CPU
SUPERVISOR LANE / CPU
Boot and self-check: read bank IDs.
Load gains, limits, filter and timer settings.
Start calibration; arm/disarm.
Watch status and faults; log telemetry.
Serve timer and fault interrupts.
Later, run higher-level behaviour.
REAL-TIME LANE / HARDWARE
Read sensor → compute PID → generate PWM
Switch off motors on a fault
The CPU does not perform these tasks.
The CPU can be slow, busy or even crash without the balance loop losing its timing. The watchdog notices a stalled CPU.

## Slide 42
CORE SELECTION
CPU OPTIONS COMPARED AND OUR DECISION
Criteria: open licence; readable SystemVerilog accepted by Vivado and Cadence tools; active maintenance; verification maturity; small and simple; clean memory interface; FPGA- and ASIC-friendly register-file options; RISC-V toolchain support.
CORE | STYLE | LANGUAGE | REMARK |  |  |  | 
Ibex (lowRISC), chosen | RV32IMC, 2-stage | SystemVerilog | open, actively maintained, well documented [R8] |  |  |  | 
CV32E40P (OpenHW) | RV32IMC(F), 4-stage | SystemVerilog | capable, but more complex than a supervisor needs |  |  |  | 
SCR1 (Syntacore) | RV32 | SystemVerilog | viable, smaller ecosystem |  |  |  | 
PicoRV32 | RV32IMC | Verilog | compact, but development has wound down; check status |  |  |  | 
NEORV32 | RV32 | VHDL | mixed-language complicates the Cadence flow |  |  |  | 
MicroBlaze | proprietary | FPGA-vendor IP | tied to the FPGA vendor; cannot move into an RTL-to-GDSII flow |  |  |  | 
 |  |  |  | Arm Cortex-M class | Arm | licensed IP | closed and licensed
Decision: Ibex, "small" configuration.

## Slide 43
IBEX / LOWRISC
IBEX: OVERVIEW AND SPECIFICATIONS
The core
Small, efficient 32-bit, in-order RISC-V core; 2-stage pipeline; RV32IMC; SystemVerilog; heavily parametrisable [R8].
Originated as "Zero-riscy" in the PULP project. Now maintained by lowRISC; production-quality, used in OpenTitan. Documentation on ReadTheDocs; Apache-2.0 licence.
Features
Machine-mode privilege; timer/external/software interrupts; 15 fast interrupts; non-maskable interrupt; simple request/grant memory interfaces.
RV32IMC
RV32: 32-bit RISC-V, 32-bit addresses and registers.
I: base integer set, 32 registers x0 to x31.
M: multiply and divide.
C: compressed 16-bit instructions, smaller code.
PUBLISHED "SMALL" CONFIGURATION [R8]
About 2.47 CoreMark/MHz
About 24 kGE (commercial estimate); ≈ 26–27 kGE (Yosys, latch register file)

## Slide 44
CONFIGURATION / PINNED RELEASE
THE IBEX "SMALL" CONFIGURATION IN DETAIL
Same documentation: "micro" about 0.9 CoreMark/MHz (about 15 kGE); "maxperf" about 3.13 CoreMark/MHz (about 30 kGE) [R8]. Small is the balanced middle. We pin one release and copy the parameter set from Ibex's own ibex_configs.yaml.
PARAMETER | "SMALL" SETTING | WHY IT SUITS US
ISA | RV32IMC (RV32E off, 32 registers) | enough for firmware; compressed code saves ROM
Pipeline | 2 stages (fetch, decode/execute) | simple, easy to reason about
Multiplier/divider | RV32MFast, 3-cycle multiply | PID runs in hardware, no single-cycle multiply needed
Instruction cache | off | predictable timing, less area
Register file | flip-flop in the named config; FPGA/latch variants exist | flip-flop/FPGA version on the Arty; evaluate latch version for layout
Extras (PMP, bit-manipulation, branch-target ALU) | off in the small config | not needed for a supervisor
Performance | about 2.47 CoreMark/MHz, about 120 CoreMark at 50 MHz | plenty for configuration and monitoring
Area | about 24 to 27 kGE | keeps layout effort modest

## Slide 45
ARCHITECTURE / TWO-STAGE CORE
IBEX ARCHITECTURE AND BLOCK DIAGRAM

## Slide 46
ARCHITECTURE / TWO-STAGE CORE
IBEX ARCHITECTURE AND BLOCK DIAGRAM
IF: instruction interface; program counter; prefetch buffer/FIFO; compressed-instruction expander. Prefetch fetches ahead.
ID/EX: decoder turns bits into control signals; controller handles stall/flush and exceptions; operand muxes and forwarding; ALU for add, shift, logic and compare; multiplier/divider; load/store unit.
Decode and execute share one stage. Results write back to the register file, which holds 32 fast registers. ALU and mult-div do arithmetic.
LSU: data interface; the only way the CPU reaches memory and our hardware registers.
CSRs: machine-mode status, interrupt enable/pending, trap vector and counters; interrupt inputs enter here. CSRs handle interrupts, traps and counters.
IBEX_TOP
ibex_core
IF
ID/EX → write back
LSU
CSR
Register file
x0 to x31
Instruction · Data · Interrupt

## Slide 47
EXECUTION / MEMORY-MAPPED I/O
HOW IBEX EXECUTES AND CONNECTS TO OUR SOC
Instruction path: PC → instruction port → ROM → IF stage → decode/execute → write back. Boot: reset vector at 0x80 in ROM.
01
Firmware
Store Kp,Ki & Kd to the PID bank address.
02
Load/store unit
Raise a data request.
03
Bus decoder
Select the PID register bank.
04
PID register
Value lands; hardware PID uses it on the next sample.
Handshake and cost
Request → grant (same cycle) → response valid (next cycle).
Simple ALU ops about 1 cycle; multiply 3 cycles; memory accesses follow the handshake.
Interrupts → Ibex
Timer interrupt (about every 100 ms) and fault interrupt wired to Ibex's interrupt inputs.
The core jumps through the vector table at the base address.

## Slide 48
FIRMWARE / BRING-UP
FIRMWARE AND BOOT SEQUENCE
01
Reset vector, startup code: set stack, copy initialised data, clear zeroed data.
02
main(): read all six bank IDs; compare with expected values.
03
Configure timer and I²C; wait for sensor init.
04
Start gyro calibration; wait for done.
05
Load Kp / Ki / Kd, setpoint, limits. Output limit starts low.
06
Set safety thresholds, enable watchdog, arm.
07
Loop: kick watchdog, log telemetry, handle interrupts, apply the re-arm policy after a fault.
Build flow
RISC-V GCC (rv32imc) → binary → ROM initialisation file → loaded into the FPGA.
Bring-up ladder
Read IDs → RAM test → LED → timer interrupt → raw IMU registers → full boot.

## Slide 49
PART E
APPLICATIONS &
ARCHITECTURE SCOPE

## Slide 50
WHERE THIS ECU CAN BE USED
Self-balancing / inverted pendulum
Direct target: two-wheeled balancing robots, mobility-scale prototypes, control-teaching rigs.
Bipedal / legged robots
Posture and balance need the same fixed-latency sensor-to-actuator path. A building block, not a full gait controller.
Autonomous rovers / mobile robots
Wheel-motor control, chassis stabilisation, fault-safe motor shutdown; supervisory CPU for mission logic.
Automotive / industrial control units
Body/chassis-class and motor-control functions. Hardware loop plus supervisory CPU mirrors current ECU architectures [R13][R14].
Drones / camera gimbals
Attitude stabilisation.
Education / research
Open, inspectable reference for ECU and SoC design.
Our demonstrator is the two-wheeled balancing robot; the others describe where the architecture applies.

## Slide 51
ADAPTING THE ECU (FUTURE SCOPE)
Other sensors: SPI IMUs, wheel encoders, distance sensors.
More control channels: replicate the PID block, e.g. one per joint or axis.
Outer loops: speed or position control in firmware on top of the balance loop.
Communication: UART or CAN for commands and logging.
Better estimation: Kalman filter block.
Other motors: different driver stages behind the same motor interface.
Because everything is register-configured, many changes are firmware or small-block changes, not a redesign.
ECU
Register-configured
+ new block: sensors
+ new block: PID channels / Kalman filter

## Slide 52
PART F
HARDWARE
& TOOLS

## Slide 53
HARDWARE / STAGED BRING-UP
HARDWARE SETUP
MPU-6050 breakout on I²C: SCL/SDA, 3.3 V, via a Pmod/header.
Two BTS7960 modules receive PWM and enable from the FPGA; each drives one DC motor.
Separate motor battery; common ground with logic.
Switches/LEDs: arm switch, E-stop button, status LEDs.

## Slide 54
HARDWARE SPECIFICATIONS
ITEM | KEY SPECIFICATIONS | 
Arty A7-100T (Digilent) [R15] | Xilinx XC7A100T-1CSG324: 101,440 logic cells, 15,850 slices, 4,860 Kb block RAM, 240 DSP slices, 4 Pmod connectors + Arduino-style header, 256 MB DDR3L, 16 MB Quad-SPI flash, USB-JTAG, powered from USB or 7 to 15 V, supported by Vivado WebPACK | 
MPU-6050 | 3-axis accelerometer + 3-axis gyroscope, 16-bit ADCs, I²C up to 400 kHz, programmable ranges (we use ±2 g, ±250 °/s), on-chip digital low-pass filter | 
BTS7960 module ×2 [R9] | PWM up to 25 kHz, 5.5 to 27.5 V, about 43 A typical current limit, integrated protections | 
Motors, chassis, battery | two DC geared motors on a two-wheeled chassis; ratings to be finalised | 
Our design is small relative to the device; actual utilisation will be reported after implementation. Other boards can be used: only pin constraints and the clock source change.

## Slide 55
SOFTWARE AND EDA TOOLS
ACROSS THE WHOLE JOURNEY
PYTHON MODEL
VIVADO SIM
VIVADO FPGA
GENUS
INNOVUS
GDSII
STAGE | TOOL
RTL entry, simulation | Xilinx Vivado (xsim)
FPGA synthesis, implementation, bitstream | Vivado (Artix-7)
On-chip debug | Vivado ILA / VIO, logic analyser, oscilloscope
Clock generation | Vivado Clocking Wizard (MMCM)
Reference models, plots | Python (golden models, matplotlib)
Firmware | RISC-V GNU toolchain (rv32imc), Make
Code quality | Verilator lint, Git/GitHub with pull-request reviews
Logic synthesis (RTL to gates) | Cadence Genus
Place and route (gates to layout) | Cadence Innovus
Further checks | other Cadence tools as available in the lab

## Slide 56
PART G
PLAN
VERIFICATION
WRAP UP

## Slide 57
DEVELOPMENT WORKFLOW
Code the block against the frozen interface
Simulate and verify it alone (self-checking testbench + golden model)
FPGA-test it alone, typical and extreme conditions
Combine blocks one by one: simulate each combination, then FPGA-test it
Full ECU: simulate, verify, FPGA test
Only then move to RTL-to-GDSII
Rule: nothing moves to the next stage until it has passed the current one. The CPU track runs alongside through all stages, until it is stable.

## Slide 58
VERIFICATION STRATEGY: SIMULATION
4
LEVEL 4 · WITH CPU
3
LEVEL 3 · FULL DATAPATH
2
LEVEL 2 · PAIRS
1
LEVEL 1 · BLOCK
Level 1, block: self-checking testbench per block; directed and random vectors; compare with a Python model.
Level 2, pairs: adjacent blocks connected: I²C to pipeline; pipeline to PID; PID to PWM.
Level 3, full datapath: MPU-6050 behavioural model, whole chain, PWM, with a simple pendulum model closing the loop.
Level 4, with CPU: Ibex running real firmware through the real bus.
Checks built in: assertions (e.g. never both PWM outputs high), reset behaviour, boundary values, saturation, injected errors (NACK, timeout, bad address).
Hygiene: lint with zero unexplained warnings; regression script; results logged per block.

## Slide 59
FPGA TEST PLAN
STAGES A TO D
Stage A: each block alone on the board using test fixtures and ILA/VIO.
Stage B: blocks combined one by one: I²C + pipeline, + PID, + PWM, + safety.
Stage C: full hardware loop (no CPU) with the robot on a stand.
Stage D: full ECU with CPU and firmware.
Typical operation: normal tilt, normal gains.
EXTREME CASES, SAFETY AND FAULTS
Extreme cases: maximum and minimum inputs, saturation, noisy readings, different I²C speeds, back-to-back events, reset during operation, power-up sequence, long-run soak.
Safety and faults: every fault alone and combined, glitch rejection, E-stop, watchdog, re-arm sequence, unplugging the sensor.
Pass criteria and logs defined per test so nothing stays half-tested.

## Slide 60
RTL-TO-GDSII FLOW (CADENCE)
RTL
Freeze + lint
Genus
Synthesis
Netlist
Simulation
Innovus
Layout
Checks
Analysis
GDSII
Export
RTL freeze, lint, constraint definition (clock, input/output timing)
Logic synthesis, Genus: RTL to gate-level netlist; area and timing reports
Gate-level simulation of the netlist
Innovus: floorplan, placement, clock-tree synthesis, routing
Final timing and power analysis; layout design-rule and connectivity checks
Export the GDSII layout and reports
Prepared from day one: single clock, fully synchronous design, no latches (except an evaluated register-file option), no FPGA primitives inside the RTL, parameterised memories.
Decisions deferred to this phase: memory implementation, target frequency, constraint tuning.

## Slide 61
PART H
TIMELINE
RESPONSIBILITIES
BREAKDOWN

## Slide 62
TIMELINE
(TENTATIVE AND FLEXIBLE)
Each phase starts only when the previous gate is met; dates will move if results demand it.
PHASE | PERIOD | WHAT HAPPENS | 
1. RTL + simulation | Oct to Nov 2026 | each block coded and verified alone; then combined one by one and simulated together; real-time datapath RTL ready by end of November | 
CPU track (parallel) | throughout | Ibex integration, bus and firmware worked on side by side until stable | 
2. FPGA testing | Nov 2026 to end Jan / early Feb 2027 | blocks alone, combined, full ECU, including safety and fault cases (lighter work during the December exam period) | 
3. RTL-to-GDSII | Feb to May 2027 | Genus synthesis, Innovus layout, final checks; target: done by May 2027 | 
Gates: RTL ready, FPGA validated, layout done.

## Slide 63
TEAM AND RESPONSIBILITIES
MEMBER | RESPONSIBILITY
Jatin | system architecture and integration lead; hardware PID accelerator; Ibex integration and firmware
Kaushal | I²C subsystem and MPU-6050 controller; CPU simulation harness
Dipiksha | timer / control scheduler; measurement, calibration, angle conversion, filter, error calculation
Vedam | ROM/RAM, bus interconnect, clock & reset, safety and fault monitor, firmware-to-ROM flow
Jaydev | PWM generator, motor interface, FPGA board wrapper, motor bring-up
Working method: shared interface contract, parallel block development, Git pull-request reviews, weekly checkpoints.

## Slide 64
RISKS AND MITIGATION
RISK | MITIGATION
Schedule slips | gate-based plan; essentials first; optional features (complementary filter) deferrable
CPU integration takes longer | Ibex is a proven core with a reference system; the hardware loop runs and is tested without it
Sensor noise / lag hurts balancing | selectable filter lengths, tuning registers, option of complementary filter
Tuning difficulty on the robot | tune on a stand with low output limits; log every run
Bugs in safety logic | independent monitor, exhaustive fault tests, peer review
Interface mismatches between blocks | frozen interface contract and pair-integration tests
Memory/area concerns in the layout flow | small memories, decisions deferred and documented

## Slide 65
EXPECTED OUTCOMES AND CONCLUSION
EXPECTED OUTCOMES (TARGETS)
A verified, documented library of ECU blocks and a complete SoC design
An FPGA demonstration of the hardware control loop on a two-wheeled robot, with measured loop timing, latency and fault-response numbers
Layout-flow results and reports
Open documentation others can learn from
CONCLUSION
Balance control is a hardware pipeline; a small RISC-V CPU configures and supervises; safety is independent of software
Ibex "small" gives an open, compact and well-documented supervisor
Verification is staged (block, combination, full ECU) in simulation and on FPGA before any layout work

## Slide 66
REFERENCES
[R1] J. Ordóñez Cerezo, Control System in Open-Source FPGA for a Self-Balancing Robot, Electronics 8(2):198, 2019 (earlier thesis: gsyc.urjc.es, 2018)
[R2] Experimental Design and Performance Analysis of a Self-Balancing Robot Using PID Control, ICM³ 2026
[R3] R. Langley, Development of a Self-Balancing Robot Utilizing FPGA, Murdoch University honours thesis, 2016
[R4] I. Abdel-Hady et al., PID Controller Design and Implementation for Multibody Mechatronic Systems, Benha Journal of Applied Sciences 10(4), 2025
[R5] Undip final project: PID with fuzzy tuning, ATMega16 + MPU-6050
[R6] A Survey of FPGA-Based Robotic Computing, IEEE
[R7] Towards a RISC-V Open Platform for Next-generation Automotive ECUs, arxiv.org/abs/2307.04148
[R8] lowRISC Ibex: github.com/lowRISC/ibex and ibex-core.readthedocs.io
[R9] Infineon BTS7960 datasheet, Rev. 1.1 (2004)
[R10] TI C2000 control law accelerator: electronicdesign.com; TI Piccolo F2805x announcement (eepower.com)
[R11] How does RISC-V fit into automotive systems?, microcontrollertips.com
[R12] Codasip/IAR, Driving ASIL-grade innovation: motor control performance and safety
[R13] SignOff Semiconductors REV-E dual-core RISC-V controller, electronicsforu.com
[R14] Infineon, Harnesses the Power of RISC-V for Next-Generation Automotive MCU Innovation, riscv.org/blog (2024)
[R15] Digilent Arty A7-100T product page, digilent.com

## Slide 67
THANK YOU
Questions & Discussion
ECU_SOC | RISC-V BASED ECU FOR A SELF-BALANCING ROBOT